## Slide 1
CMPG325 NETWORK
IMPLEMENTATION PROJECT
Iketsetseng Private School | Mahikeng
Project ID: CMPG325-2026-022 • Client ID: CLI-022
Addressing block: 192.168.21.0/24
Presented by: Miss N Khumalo
Student number: 42606152
WIRELESS SECURITY • VLAN SEGMENTATION • TESTING

## Slide 2
Client requirements and design response
The design focuses on secure, segmented connectivity and additional-floor coverage.
Client needs
• Connect staff, students and administration
• Use 192.168.21.0/24
• Provide local DHCP and DNS services
Assigned requirements
• Wireless security: WPA2-PSK with AES
• Add coverage to another floor/area
• Minimise unnecessary Internet bandwidth use
Design approach
Router-on-a-stick routing, VLAN separation, a managed switch, local services and three wireless access points address the key requirements.
CMPG325 • Iketsetseng Private School

## Slide 3
Network topology
CMPG325 • Iketsetseng Private School
1qesx

## Slide 4
Network layout and IP addressing
VLANs separate logical groups and make the network easier to manage.
R1-Edge Router
SW-Core Switch
SRV-DHCP-DNS
AP-Staff + AP-Student
AP-Additional- Floor
Router-on-a-stick: VLAN subinterfaces route between internal networks.
VLAN | Purpose | Network / mask | Default gateway
10 | Staff | 192.168.21.0/26 | 192.168.21.62
20 | Students | 192.168.21.64/26 | 192.168.21.126
30 | Admin / Servers | 192.168.21.128/27 | 192.168.21.158
99 | Management | 192.168.21.192/28 | 192.168.21.193
CMPG325 • Iketsetseng Private School

## Slide 5
Wireless security and additional-floor coverage
The additional-floor change request was addressed with a third student access point.
Staff Wi-Fi
SSID: Iketsetseng-Staff
Security: WPA2-PSK
Encryption: AES
Student Wi-Fi
SSID: Iketsetseng-Student
Security: WPA2-PSK
Encryption: AES
Additional-floor Wi-Fi
SSID: Iketsetseng-Student-Floor2
Security: WPA2-PSK
Encryption: AES
Security test
An incorrect Wi-Fi password caused the client to disconnect.
Coverage change
AP-Additional-Floor connects to SW-Core Fa0/4 in VLAN 20.
CMPG325 • Iketsetseng Private School

## Slide 6
Core configuration and services
Central services support automatic addressing and local name resolution.
DHCP on R1-Edge
Pools: STAFF_POOL, STUDENT_POOL and ADMIN_POOL.
Clients receive an IP address, gateway and DNS settings.
Local DNS server
SRV-DHCP-DNS: 192.168.21.130/27
Gateway: 192.168.21.158
www.iketsetseng.local → 192.168.21.130
Switch configuration
VLANs 10, 20, 30 and 99. Gi0/1 is the 802.1Q trunk to R1-Edge.
Bandwidth-conscious design
Local services and internal traffic can stay within the school network, avoiding unnecessary Internet dependence.
CMPG325 • Iketsetseng Private School

## Slide 7
Key test evidence
Screenshots from Packet Tracer confirming connectivity, VLAN trunking and local DNS.
CMPG325 • Iketsetseng Private School
Server to gateway
SRV-DHCP-DNS pings 192.168.21.158: 4 sent, 4 received, 0% loss.
Server to VLAN gateways
Pings to 192.168.21.126 and 192.168.21.62 both reply 4/4 with 0% loss.
VLANs and trunk
SW-Core Gig0/1 is an 802.1Q trunk carrying VLANs 10, 20, 30 and 99, all active.
Local DNS record
DNS service on: www.iketsetseng.local resolves to 192.168.21.130.

## Slide 8
Testing and results
Tests were performed in Packet Tracer using client command prompts and device CLI.
Test | Observed result | Status
Staff DHCP | 192.168.21.11 | PASS
Student DHCP | 192.168.21.75 | PASS
Additional-floor DHCP | 192.168.21.77 | PASS
Staff gateway / server | 4/4 replies to .62 and .130 | PASS
Student gateway / server | 4/4 replies to .126 and .130 | PASS
Additional-floor gateway / server | 4/4 replies to .126 and .130 | PASS
Local DNS | www.iketsetseng.local resolved to 192.168.21.130 | PASS
Wrong Wi-Fi password | Client disconnected from secured SSID | PASS
CMPG325 • Iketsetseng Private School

## Slide 9
Conclusion
The implementation addresses the main internal networking requirements in the project brief.
What was achieved
• VLAN-based segmentation
• DHCP address assignment
• Local DNS resolution
Assigned feature
• WPA2-PSK/AES on three SSIDs
• Wrong-password rejection tested
• Additional-floor AP added to VLAN 20
Limitation to report accurately
Local services and segmented traffic reduce avoidable Internet use. Public Internet reachability was not proven by the recorded tests.
Thank you
CMPG325 • Iketsetseng Private School